## Slide 1: Introduction to CPU and Memory Buses

## Slide 2: What is a bus ?
A bus is a collection of wires and connectors through which different types of data are transmitted.
Each wire is called a line

## Slide 4: Buses Inside a Computer
There are different types of computer busses:
Data bus
Address bus
Control bus

## Slide 5: Data Bus
Carries data between the CPU and memory or I/O devices
Bi-directional
  Data transferred “out of” the CPU for write operations
  Data transferred “into” the CPU for read operations
Typical sizes: 8, 16, 32, 64 lines
Signal names:
  D0, D1, D2, D3, etc.

## Slide 6: Address Bus
Carries an address from the CPU to Memory or I/O devices
Unidirectional
  The address is always supplied by the CPU
    (There is one exception to this, which we’ll discuss later.)
Typical sizes: 16, 20, 24 lines
Signal names:
  A0, A1, A2, A3, etc.

## Slide 7: Control Bus
Collection of signals for coordinating CPU activities
Each signal has a unique purpose
Typical sizes: 10-20 lines
Signals are output, input, or bi-directional
Typical signals
  /RD (read)
  /WR (write
  CLK (clock)
  /IRQ (interrupt request)
  etc.

## Slide 8: Synchronous Bus vs. Asynchronouse Bus
A bus can be classified as one of two type: synchronous and asynchronous.
Synchronous bus: there is a common clock that synchronizes bus operations.
  Includes a clock in the control lines
  A fixed protocol for communication that is relative to the clock
  Advantage: involves very little logic and can run very fast
  Disadvantages:
    Every device on the bus must run at the same clock rate
    To avoid clock skew, they cannot be long if they are fast

## Slide 9: Continue ..
Asynchronous bus: there is no common clock. Bus master and slaves have to “handshake” during transmission process.
  It is not clocked
  It can accommodate a wide range of devices
  It can be lengthened without worrying about clock skew
  It requires a handshaking protocol

## Slide 10: Measurement
Bus width: indicates the number of wires in the bus for transferring data.
Bus bandwidth: refers to the total amount of data that can theoretically be transferred on the bus in a given unit of time.

## Slide 11
Bus | Width (bit) | Bandwidth (MB/s)
16-bit ISA | 16 | 15.9
EISA | 32 | 31.8
VLB | 32 | 127.2
PCI | 32 | 127.2
64-bit PCI 2.1 (66 MHz) | 64 | 508.6
AGP 8x | 32 | 2,133
USB 2 | 1 | Slow-Speed: 1.5 Mbit/s Full-Speed: 12 Mbit/s Hi-Speed: 480 Mbit/s
Firewire 400 | 1 | 400 Mbit/s
PCI-Express 16x version 2 | 16 | 8,000
Width and Bandwidth of Some Typical Buses

## Slide 12: Advantages of Buses
Versatility:
  New devices can be added easily
  Peripherals can be moved between computer systems that use the same bus standard
Low Cost:
  A single set of wires is shared in multiple ways
Memory
Processor
I/O Device
I/O Device
I/O Device
Notes: The two major advantages of the bus organization are versatility and low cost.
By versatility, we mean new devices can easily be added.
Furthermore, if a device is designed according to a industry bus standard, it can be move between computer systems that use the same bus standard.
The bus organization is a low cost solution because a single set of wires is shared in multiple ways.
+1 = 7 min. (X:47)

## Slide 13: Disadvantages of Buses
It creates a communication bottleneck
  The bandwidth of that bus can limit the maximum I/O throughput
The maximum bus speed is largely limited by:
  The length of the bus
  The number of devices on the bus
  The need to support a range of devices with widely varying data transfer rates
Memory
Processor
I/O Device
I/O Device
I/O Device
Notes: The major disadvantage of the bus organization is that it creates a communication bottleneck. When I/O must pass through a single bus, the bandwidth of that bus can limit the maximum I/O throughput.
The maximum bus speed is also largely limited by:
(a) The length of the bus.
(b) The number of I/O devices on the bus.
(C) And the need to support a wide range of devices with a widely varying latencies and data transfer rates.
+2 = 9 min. (Y:49)

## Slide 14: Instruction Cycle
Two phases:
  Fetch
  Execute

## Slide 15: Continue ..